| Readiness code | Average Wind speed | Gust Speed | Activity Guidance | General Guidance |
| --- | --- | --- | --- | --- |
| Green | Below 17 mph (27 kph) | 25 mph (40 kph) or below | Safe for all site operations | Maintain good housekeeping. |
| Yellow | 17 mph or above (27 kph) | 26 mph (42 kph) | Be aware, You may want to consider stopping external working at height | Check ground level storage/ housekeeping. On exposed sites take extreme care with all roofing operations. Maintain housekeeping. |
|  | 23 mph or above (37kph) | Or above 35 mph (56 kph) or above |  | Check roofs for loose objects, maintain housekeeping. Extra care with lifting operations. You may want consider stopping lifting operations. |
| Red | 38 mph or above (61 kph) | 38 mph or above (61 kph) | Take action, Stop all external working at height | Check scaffolds, roofs for loose materials, missing ties. Secure scaffold boards, sheeting, if appropriate |
|  | Average 45 mph (71 Kph) above | or gusts of→50 mph (80 kph) or |  | If there are external materials that could be blown around such as sheet materials & rubbish. If in doubt stop work |