Scaffold Specification

All scaffolds should comply with best practise and Guidance issued by the National Access and Scaffolding Confederation (NASC).

The following guidance should be used:

- Technical Guidance TG20:13 Tube fitting scaffold.

- NASC guidance SG4:15 for tube and fitting scaffold.

For any scaffold falling outside the scope of ‘standard configuration, the scaffold must have been designed for the purpose intended.

### Scaffold structures that need to be designed

- All shoring scaffolds (dead, raking, flying).

- Cantilevered scaffolds.

- Truss-out Scaffolds.

- Façade retention

- Access scaffolds with more than the 2 working lifts.

- Buttressed free-standing scaffolds.

- Temporary roofs and temporary buildings.

- Support scaffolds.

- Complex loading bays.

- Mobile and static towers.

- Free standing scaffolds.

- Temporary ramps and elevated roadways.

- Staircases and fire escapes (unless covered by manufacturers instructions).

- Spectator terraces and seating stands.

- Bridge scaffolds.

- Towers requiring guys or ground anchors.

- Offshore scaffolds.

- Pedestrian footbridges or walkways.

- Slung and suspended scaffolds.

- Protection fans.

- Pavement gantries.

- Marine scaffolds.

- Boiler scaffolds.

- Power line crossings.

- Lifting gantries and towers.

- Steeple scaffolds.

- Radial / splayed scaffolds on contoured facades.

- System scaffolds outside manufacturers guidance.

- Sign board supports.

- Sealing end structures (such as temporary screens).

- Temporary storage on site.

- Masts, lighting towers and transmission towers.

- Advertising hoardings/banners.

- Rubbish chute.

- Any scaffold structure subject to:

  - Vibration

  - High Loading

  - Long term duration

  - High risk areas

  - Loading from passenger/goods hoists

any scaffold structure not mentioned above that falls outside the ‘compliant scaffold’ criteria in TG20 or similar guidance from manufacturers of system scaffolds.

Note: The above list is not exhaustive and any scaffold that is not a standard configuration or does not comply with published manufacturers’ guidelines will require a specific design produced by a competent person.

- All Scaffolds must be tagged with an appropriate tagging systems.

- All scaffolds should be inspected every 7 days or after inclement weather, any defects found during the inspection must be reported and records of the inspection must be kept.

- The top guardrail should be a minimum of 950mm above the working platform and any gap between the top rail and the intermediate rail should not exceed 470mm.  Toe boards to be suitable and sufficient to prevent people or materials from falling.

- All ladder openings must be protected Trapdoor / gate, etc.

- Property occupants must be able to open their windows and doors fully.

- All building access must be double scaffold boarded.

- Specific consideration of security is required and steps must be taken to prevent unauthorised access to scaffold via fencing, netting of other means.

- Generally scaffold must be netted, to protect members of the public.

- The scaffold must be designed and built to take any loading with respect to the work such as materials etc.

- Scaffold must not be adapted unless done so by qualified scaffolder, and signed off as safe to use.

- Adaption’s to scaffold must also be signed off by the manager or supervisor after any adaption takes place.

- No work will be undertaken on any scaffold with out the correct sign off certification.

- Once works are complete the manager will notify the scaffolder that works are complete, so the scaffold can be dismantled.